## Slide 1
2
INSIGHTS
What we learned before building
Where a tonne's carbon comes from
Chart: 
| Raw material (Scope 3) | Electricity (Scope 2) | On site (Scope 1)
share | 1.612 | 0.832 | 0.443
2.89
tCO₂e / tonne
Raw material (Scope 3)
56%
Electricity (Scope 2)
29%
On site (Scope 1)
15%
WHAT WE FOUND
SO CARBONSPARK…
1
The raw material matters most
Each extra point of scrap saves ~35 kg CO₂e per tonne.
puts scrap vs virgin first
2
Electricity is the next big lever
Coal power emits ~85× more per kWh than wind.
lets you build the grid mix, source by source
3
Some levers barely matter
Grid + scrap save ~0.6 t/t; rail + technology under 0.05.
ranks the levers, biggest first
4
“Practical” has limits
Stainless needs virgin chromium and nickel; coal can't vanish overnight.
optimises within realistic limits
Notes: Insights are what we learned from studying the problem, and each one explains a design choice. The doughnut is one tonne from a typical electric-arc stainless route: 56% of its carbon comes with the raw material, 29% from purchased electricity, 15% burned on site. One: the raw material matters most; every extra point of scrap saves about 35 kg per tonne, so scrap versus virgin is the first control in CarbonSpark. Two: electricity is next; coal power emits about 85 times more per kWh than wind, so users build the grid mix source by source. Three: not every lever is worth chasing; grid and scrap together are worth about 0.6 t/t, rail and technology under 0.05, so the tool ranks levers biggest first. Four: practical has limits; stainless still needs virgin chromium and nickel and no plant can drop coal overnight, so the optimiser works within realistic limits.