## Slide 1
Notes: Title slide — left blank deliberately. Add team name, members, college and the problem statement title here.

## Slide 2
1
PROBLEM UNDERSTANDING · OBJECTIVES
Emissions are decided long before anyone can see them
A stainless tonne's carbon is fixed by four choices — how much scrap is charged, which grid supplies the furnaces, how the material is hauled, and which technology each stage runs. Those choices are made by planners and buyers who have no number in front of them at the moment of deciding. The workbook that holds the coefficients is an audit artefact, not a decision tool.
WHY IT MATTERS
Scope 2 — purchased electricity — is 56% of the baseline tonne. The single biggest lever is a procurement decision, not a metallurgical one.
Scrap displaces virgin chromium and nickel, but grade requirements cap how far it can go. The trade-off is real and currently unquantified at the plant.
Net Zero by 2050 needs the marginal question answered in seconds: what does this change do to the tonne?
OBJECTIVES — MEASURABLE
Model every process step in the JSL grid — 67 routes across 8 departments — not a lumped plant average.
Report Scope 1, 2 and 3 separately, per GHG Protocol, and reconcile to the workbook exactly.
Respond to an input while it is being dragged, not after it is released.
Return a lower-carbon configuration the plant can actually contract — and say what it would take.
THE TONNE TODAY
6.167
tCO₂e per tonne — workbook default route, 40% scrap, today's Indian grid
56%
of that total is Scope 2 alone (3.451 tCO₂e/t)
47.4
GJ/t specific energy at the same baseline
67
process routes carrying their own Scope 1/2/3 coefficients
Notes: Open on the decision gap, not on the technology. The point of this slide: the emissions of a tonne are determined by four choices, and none of the people making them can see the consequence at the time. Numbers are from our own model run on the supplied workbook: the default route (40% scrap, today's Indian grid, first-listed technology at every stage) gives 6.167 tCO2e/t and 47.4 GJ/t. Scope 2 at 3.451 t/t is 56% of the total — say this out loud, it is the reason the grid-mix slider is the centrepiece of the tool. The objectives are deliberately measurable so the validation slide can be checked against them one by one.

## Slide 3
2
PROPOSED SOLUTION
CarbonSpark — the workbook, made interactive
A Streamlit web application built directly on the supplied grid. Every coefficient is read from the workbook at load; nothing is re-typed, so the tool cannot drift from its source.
1
Extract
67 process rows × 8 departments parsed from the workbook, coefficients and notes kept together.
2
Model
Every metric is linear in virgin/scrap share; transport rows are bilinear in (x,y)×(rail,road). Scope 2 = kWh × grid factor.
3
Re-arrange
The route is exported to the browser as a coefficient model, so a drag is arithmetic in the page — not a server round-trip.
4
Decide
Four levers, a scenario comparison, and a feasibility-bounded optimiser over the same model.
Four levers: scrap share · grid mix · rail/road per leg · technology per stage
WHAT THE USER SEES
One headline tonne, split into Scope 1 / 2 / 3
Inputs in a docked panel, never a page away
Figures and charts follow the slider live
Per-process table behind every number
Notes: This is the 'how'. Three things to land. First: the tool reads the workbook itself at load — no coefficient is re-typed, so it cannot drift from the source of truth. Second: the model is not a black box — every metric is linear in the virgin/scrap split, and the two transport rows are bilinear in (virgin/scrap) x (rail/road), which is what makes the whole thing exactly re-arrangeable. Third, the differentiator: because it is exactly re-arrangeable, we export the current route to the browser as a coefficient model, so while a slider is being dragged the figures AND the Plotly bars recompute in the page. Streamlit only commits a slider on release; without this the tool feels dead under the hand. The screenshot shows the docked Inputs panel — scrap ratio and haulage split — over the live readout.

## Slide 4
3
VALIDATION · FEASIBILITY · ASSUMPTIONS
What is buildable, not what is imaginable
SCENARIO | tCO₂e/t | vs JAJPUR | WHAT IT ASSUMES
Workbook default route | 6.167 | +34.1% | 40% scrap · Indian grid today
JSL Jajpur — reference | 4.598 | — | 35% scrap · 29 stages · 0.762 kg/kWh
JSL Hisar as configured | 4.669 | +1.5% | 45% scrap · 31 stages
Buildable today | 2.089 | −54.6% | 60% scrap · grid 0.439 · coal held ≥45%
Stretch, but reachable | 1.205 | −73.8% | 80% scrap · grid 0.111 · firmed renewables
Theoretical floor | 0.821 | −82.2% | 100% scrap · non-fossil grid · any technology
HOW WE KNOW IT IS RIGHT
37 automated tests, including a full re-derivation of the workbook totals.
The browser's live model matches the server to 1×10⁻⁹ across four scenarios and every department.
All 65 Scope-2 rows reconcile to their stated kWh and grid factor.
Global warming potentials are IPCC AR5; grid factors are AR5 lifecycle medians.
ASSUMPTIONS & LIMITATIONS
The workbook's gas columns carry Scope 1 only (~10% of the scope total) — we report them as such rather than as a full gas split.
Its electricity intensities are high against public figures (EAF 1,668 kWh/t vs a typical 450–700). Absolute values are therefore indicative; differences between scenarios are robust.
Plant profiles are built from public disclosures, not an equipment inventory. Jajpur's source-wise grid split is an estimate.
WHY THREE LEVELS
An unbounded search lands on 100% scrap and a 100% wind grid and tells the plant nothing. Each level carries its own explicit limits — a coal floor because the grid a plant is connected to is coal-fired, a scrap cap because stainless needs virgin chromium and nickel, and no vacuum or remelting routes, which carry a negligible share of world tonnage. The tool states the reasoning for every limit on screen.
Notes: This is the evidence slide — spend the most time here. Every row is quoted against Jajpur as we model it (4.598 t/t), the same reference the tool uses on screen. The workbook's own default route sits 34% above it; Hisar is 1.5% above, so the two sites are close. Then the three optimiser levels. The key defence: 'Buildable today' at 2.089 t/t (-54.6%) holds coal at 45% or more of supply and caps hydro and nuclear near their real grid share, because an industrial consumer cannot contract unlimited amounts of either. That is what makes it a feasible answer rather than a hypothetical one. On validation, the strongest single fact is the 1e-9 agreement between the browser model and the server — the live figures are the same arithmetic, not an approximation. Be upfront about the limitations; the electricity intensities in the supplied workbook are high against public benchmarks, which is exactly why we present deltas rather than certified absolutes.

## Slide 5
4
INNOVATION · DIFFERENTIATION · EXPECTED IMPACT
What this does that a spreadsheet cannot
Live, not lagged
The route is re-arranged into coefficients and evaluated in the browser, so figures and charts track the slider mid-drag — exact to 1×10⁻⁹, not an approximation.
Feasible, not fantastical
Three ambition levels with stated economic and grid limits, so the answer is something a plant can put in a procurement plan.
Scenario against scenario
Any two configurations compared side by side — baseline, the live plant, or two of the user's own — with per-scope deltas.
Auditable to the row
Every headline opens into the per-process table and the workbook's own coefficient notes.
EXPECTED IMPACT — AT 1 Mt OF OUTPUT
2,508
kt CO₂e avoided per year on the buildable path
−28.3%
specific energy, 33.9 → 24.3 GJ/t
−65.0%
Scope 2, the largest single component
Built on the supplied workbook · Streamlit · open to any plant configuration
Notes: Close on differentiation and impact. The one thing to say if you only get one sentence: every other calculator recomputes on the server after you let go of the control — ours re-arranges the model into coefficients and evaluates it in the page, so the number moves with your hand and is still exact to 1e-9. Second differentiator is the feasibility framing, which answers the brief's word 'practical' directly. On impact, quote the annualised figure: at 1 Mt of output, the buildable path avoids 2,508 kt CO2e a year, cuts specific energy 28.3%, and takes 65% off Scope 2 — the component that was 56% of the tonne on slide 1. Invite them to open the tool and change any input; nothing in it is hard-coded.